## Slide 1
GPU and (Async)Solvers for Physics-based simulations
Hadrien Courtecuisse

## Slide 2
1
2
3
Overview and theoretical bases
GPU parallelization and Cuda
Preconditioners and asynchronous solvers
4
Applications
Asynchronous solvers for contact
5

## Slide 3: Equations formulation
Continuum mechanics
  Assumption of continuity of matter
  Based on physics law
  Define a deformation model
Solution based on finite element method
  Discretization in small elements
  Integrate and solve equations by elements
  Approximation which depends on the size of elements
Constitutive law
Solution of a dynamic system :
  Time evolution of deformable bodies
  Involves acceleration, velocity, and position
Strain
Stress

## Slide 4: Real time : definition
  Real-time simulation : all the computations done in 1 time step, are done in a time equal to the time step
dt
t
t+dt
Simulation time
t+1sec
User time (real)
t+1sec
t
  The number of Frame Per Second (FPS) times dt must be equal to 1 second.

## Slide 5: Real time : definition
Simulation too fast:
dt
t
t+dt
t+1sec
t+1sec
t
Slow down the simulation with a waiting loop
t+1sec
Simulation time
User time (real)

## Slide 6: Real time : definition
Simulation too slow :
dt
t
t+dt
t+1sec
t+1sec
t
Record the images of the simulation, and play them faster to reach real time.
Impossible when the user interact with the simulation !
Simulation time
User time (real)

## Slide 7: Why do we need real-time ?
Synchronize the simulated instruments with the simulated bodies
Slow down the motion of the instruments in the simulation
Difficult (impossible) to use for a surgeon
Delay when applying haptic forces
Real motion
Simulation
Deformable
structure

## Slide 8: Why do we need real-time ?
Synchronize the simulated instruments with the user motion
The velocity of the instruments is faster than other deformable structures
Important error introduced during the interaction
Real motion
Simulation
Structure déformable
Deformable
structure

## Slide 9: Why do we need real-time ?
Crash test example :
The velocity has a huge impact on the resulting deformation
Delay in the simulation introduce important errors !

## Slide 10: Real time : definition
Additional constraints :
  A frame rate of at least 60 FPS is necessary to have a visual fluidity
  Less than 20 ms to process all the computations (computation of the deformation, collision detection, contact force response, rendering, …)
Interactive simulation :
  A simulation which is not slower than real time but fast enough to allow user interactions
  At least 10 FPS
Simulation with haptic feedback
  Haptic requires at least 1Khz to simulate a smooth force feedback, ant stiff interactions
  Les than 1 ms to update haptic forces
  Accuracy ?
    It’s relatively easy to simulate very fast with very simplified models
Find a tradeoff between accuracy and computation time

## Slide 11: Interactive deformation model
Small displacements and small deformations :
  Linear constitutive law
  Simple and fast
  Inflates for large deformations/displacements
Large displacements and small deformations :
  Compensate geometrical non linearity
  Take into account the rotations / linear deformation
  Co-rotationnal model : TetrahedronFEMForceField
Large displacements and large deformations :
  Simulation of large deformation
  Hyperelastic model :
  MJED [Marchesseau et al. 2010]
  TLED [Comas et al. 2008]
  Difficult to solve in real time
Co-rotational
FEM
Linear
FEM

## Slide 12: Temporal system evolution
Explicit integration :
  Local resolution
  Fast and parallelizable
  Stability implies to use very small time steps
  Implicit integration :
  Update the acceleration from position and velocity at the end of the time step
  Stable with large time steps
  Rearranging equations gives the linear system :
  Linearization of around the initial position [Baraff et al. 1998]

## Slide 13
1
2
3
Overview and theoretical bases
GPU parallelization and Cuda
Preconditioners and asynchronous solvers
4
Applications
Asynchronous solvers for contact
5

## Slide 14: New parallel architectures
Parallelization of a simulation is not a new idea :
  Parallel processors, distributed processors, …
Real time simulation constraints :
  A lot of very fast computations
Difficult to increase the frequency of processors
  Heat dissipation
  Electric consumption
  Parallelization of algorithms
Use GPU to achieve computations (GPGPU).
  GPU is very different than CPU parallelization.
  Run thousand of threads to exploit efficiently the GPU
GPU is seen as a specialized co-processeur :
  Achieve high parallel tasks

## Slide 15: GPU architecture
GPU is seen as a specialized co-processeur :
  Achieve high parallel tasks
CPU
Kernel 1
GPU
Grille 1
Block
(0,0)
Block
(1,0)
Blobk
(2,0)
Block
(0,1)
Block
(1,1)
Block
(1,2)
Grille 2
Kernel 2
Block (1,1)
Thread
(0,0)
Thread
(1,0)
Thread
(2,0)
Thread
(3,0)
Thread
(4,0)
Thread
(0,1)
Thread
(1,1)
Thread
(2,1)
Thread
(3,1)
Thread
(4,1)
Thread
(0,2)
Thread
(1,2)
Thread
(2,2)
Thread
(3,2)
Thread
(4,3)
Two level of parallelism :
  A Grid contains several blocs
  A Block contains several threads
Run thousand of threads of threads to exploit efficiently the GPU !
GPU programing :
  Local synchronisations very fast
  Global synchronisations very slow (Synchronisation with the CPU)

## Slide 16: GPU-based implicit integration
  Parallelization of implicit integration [Allard et al. 2011, GPU Gems]
Only and are not linear algebra operations
  Accumulate forces on each DOF
Force
dForce
Only two scalar and must be transferred between CPU and GPU to check convergence
Most of operations and are linear algebra operations
  Parallelization solutions exists
+
dot
GPU
CPU

## Slide 17: Implicit solver on GPU
Accumulate forces on each points
  Independent of the deformation model
  Dependences between edges
Parallelization methods :
  Graph partitioning [Hermann et al. 2010]
  Small number of processors
  Graph coloration [PhysX, Bullet]
  Graph very sparse, analysis of the graph
Treat each DOF in parallel
  Assign an unique ID to each edge
  Pre-compute neighbourhood associations
  Require one global synchronisation
Precomputed vector of neighborhood :
Synchronisation
Kernel2
0
1
2
3
4
Temporary vector :
Kernel1

## Slide 18: Performances evaluation
Nombre
Speedup between 5 to 25
Simulate 300 000 elements in real time (CG limited to 25 iterations)
Number of elements
Speedup

## Slide 19
1
2
3
Overview and theoretical bases
GPU parallelization and Cuda
Preconditioners and asynchronous solvers
4
Applications
Asynchronous solvers for contact
5

## Slide 20: Asynchronous preconditioner
GPU-Base Conjugate gradient :
  Simulate thousand of elements in real-time
  High number of iterations for ill conditioned problems
  Non homogeneous objects / Non uniform meshes

## Slide 21: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 22: Asynchronous preconditioner
Fast convergence with additional overheads
  Overhead to inverse the preconditioner
  Overhead to apply the preconditioner at each iteration
Use a preconditioner :
  Approximation of the system which is easier to invert
New FEM Computation
CG
Iterations
Precond
Application
Precond
Computation
GPU-Base Conjugate gradient :
  Simulate thousand of elements in real-time
  High number of iterations for ill conditioned problems
  Non homogeneous objects / Non uniform meshes

## Slide 23: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 24: Asynchronous preconditioner
Fast convergence with additional overheads
  Overhead to inverse the preconditioner
  Overhead to apply the preconditioner at each iteration
Exploit time coherency between time steps
Use a preconditioner :
  Approximation of the system which is easier to invert
New FEM Computation
CG
Iterations
Precond
Application
Precond
Computation
GPU-Base Conjugate gradient :
  Simulate thousand of elements in real-time
  High number of iterations for ill conditioned problems
  Non homogeneous objects / Non uniform meshes

## Slide 25: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 26: Asynchronous preconditioner
Fast convergence with additional overheads
  Overhead to inverse the preconditioner
  Overhead to apply the preconditioner at each iteration
Exploit time coherency between time steps
Enable to use advanced preconditioners :
  Use an exact factorization of the system
  remains sparse and can be applied to detailed meshes
Use a preconditioner :
  Approximation of the system which is easier to invert
New FEM Computation
CG
Iterations
Precond
Application
Precond
Computation
Synchronization
GPU-Base Conjugate gradient :
  Simulate thousand of elements in real-time
  High number of iterations for ill conditioned problems
  Non homogeneous objects / Non uniform meshes

## Slide 27: Temporal system evolution
time
Step
Step
Step
Step
Step
Each step requiers to solve a linear system (due to non linearities)
Step
Step
Step
Step
time
Step

## Slide 28: Asynchronous Preconditioner
time
First, we precompute the factorization of the system
Step

## Slide 29: Asynchronous Preconditioner
Step
Step
Step
Step
Step
We use as preconditioner for the following steps, and in parallel we compute the next preconditioner
U
time

## Slide 30: Asynchronous Preconditioner
time
Step
Step
Step
Step
Step
As soon as is available, we swap pointers to use for the following time steps
U
U

## Slide 31: Asynchronous Preconditioner
time
Step
Step
Step
Step
Step
Step
Step
Step
Step
Step
In parallel, we factorize the next preconditioner
U
U

## Slide 32: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 33: Asynchronous preconditioner
Heuristic to limit the divergence of the préconditionneur :
  Apply rotation which appears since the last update of the preconditioner
  Limit the effect of geometrical non linearities

## Slide 34: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 35: Asynchronous preconditioner
Update the preconditioner as soon as possible :
  The computation of the preconditioner is completely hidden from the simulation point of view.
  With an optimized library, few time steps of simulation are necessary to update the preconditioner.
Heuristic to limit the divergence of the préconditionneur :
  Apply rotation which appears since the last update of the preconditioner
  Limit the effect of geometrical non linearities

## Slide 36: Asynchronous preconditioner
Number of iterations
Computation time (ms)

## Slide 37
1
5
2
3
4
Overview and theoretical bases
GPU parallelization and Cuda
Preconditioners and asynchronous solvers
Applications
Asynchronous solvers for contact

## Slide 38: Collision response
Signorini law to build a LCP (Linear Complementary Problem)
dt=0,01
avec
is the jacobian of contacts (sparse)
is a measure of the interpenetration
λ is the contact force
is the compliance matrix

## Slide 39: Preconditioners for contacts
Reuse the préconditionneur to solve contacts [Courtecuisse et al. 2011, MICCAI]
However, we don’t have but it’s factorization
  We know how to apply the preconditionneur :
LDL
  We repeat this operation until we get
  Finally we get the compliance matrix with:
Compliance
  ( is sparse)
The Compliance matrix is only a scaled version of the inverse of the system

## Slide 40: GPU parallelization
GPU
Multiprocessor
Multiprocessor
Multiprocessor
Multiprocessor
Multiprocessor
Multiprocessor
LDL
S
Each resolution is computed by a single multiprocessor
A second level of parallelism is used inside each resolution
  Well suit to GPU architectures
  Only use local synchronisations
LDL
S
LDL
S
LDL
S
LDL
S
LDL
S
The most time consumming task is the compuation of
Each column can be computed in parallel
Thread
(0,0)
Thread
(0,1)
Thread
(1,0)
Thread
(1,1)
Thread
(2,0)
Thread
(2,0)

## Slide 41: Validation of the method
dt=0,01
Update every 3 time steps on average
Compare the positions with different approximations of the Compliance
  The green shape represent the exact solution
  The object is non homogeneous : Red tetrahedra are stiffer than blue ones
With Asynchronous update of the preconditioner, we get almost the correct solution
  The green part and the blue part overlap perfectly
dt=0,01
Compliance
Warping
dt=0,01
Update every 50 time steps
dt=0,01
Update every 20 time steps

## Slide 42: Computation time on GPU
Accélération
Temps (sec)
Nombre de Contraintes
Nombre de Contraintes
With GPU implementation we can solve up to 128 constraints at the same cost
  Real time computation is very limited on CPU (less than 10 constraints)
  Enable to handle large number of contacts in real time on GPU
This method is well suit with LDI approach

## Slide 43
1
5
4
2
3
Overview and theoretical bases
GPU parallelization and Cuda
Preconditioners and asynchronous solvers
Applications
Asynchronous solvers for contact

## Slide 47
Thank you for your attention